## Slide 1: Radio Frequency (RF) Safety When Working Near Cellular Antennas
Wireline Field Technicians
January 2017

## Slide 2: Contents / Agenda
Background - deployment of small cell antennas
Radio Frequency (RF) Hazard
RF Exposure
Tech Training
RF Monitor
Next Steps

## Slide 3: Background
Cellular companies are beginning to deploy antennas on utility poles (and other non-traditional structures)
    Poles, light posts, billboards, buildings
    “Densify” their network coverage
    Verizon Wireless and other carriers
    Pole owners have an obligation to grant space / access

## Slide 4: RF Hazard
  Cellular antennas use radio waves to transmit signals.
  Radio waves are a form of electromagnetic energy and are referred to as "radio frequency" or "RF" energy or radiation
  Prolonged exposure to RF energy can increase a person’s body temperature (by causing the atoms in your body vibrate faster)
    Tissue damage may occur because of the body's limited ability to dissipate excessive heat
  RF exposure effects are not cumulative
    Multiple exposures do not add up…when exposure stops, any heating is dissipated
    At low levels of exposure or short exposure times, where significant buildup of heat does not cause damage to tissues, temporary heating of tissues will not cause lasting effects.

## Slide 5: RF Exposure
  Three factors impact the amount of RF energy a person is exposed to:
    Power level – how strong is the signal being transmitted from the antenna?
    Distance – how close is someone to the antenna, the energy level dissipates quickly over distance
    Time – how long is someone exposed to the RF energy
  Permissible Exposure Limits (PEL)
    The FCC has established two levels of PEL regarding RF radiation
      General Population Limit – for those who may not be aware of the exposure
      Occupational / Controlled Limit – for those who are aware of the hazard and can exercise control to limit their exposure

## Slide 6: Wireline Field Ops Approach
  Approve appropriate locations for deployment on poles
    Not allowed on poles with hubs or cross-boxes
    Locations with low level of tech activity are best
  All outside technicians receive training
    1Q2017
    Awareness for all technicians
    How to work in an RF environment
      How to use the RF meter, alarming, when to exit the work area
  Deploy Nardalert RF monitor – initial deployment underway, more to follow
  When working in an RF environment
    Utilize an RF meter
    If necessary, request shut-down

## Slide 7: Pole Mounted Antennas
  Three components
    The transmitting antenna
    Support equipment / electronics
    Signage
  Verizon employees are to strictly adhere to restrictions indicated by RF signage unless equipped with an RF meter so that they can monitor and control their amount of RF exposure.

## Slide 8: Contacting the Carrier NOC
  Contact all wireless carriers directly should work need to be performed within the posted separation distance or restricted RF area (where RF levels exceed the General Public Limits).
  Arrange for the antenna to be temporarily powered down before work can begin.
  Verizon Wireline personnel will not be permitted to power down any antennas directly, the carrier will be required to power down any antennas
    The contact number for the carrier is listed on the RF warning stickers or on the NOC sticker.
    When arranging for an antenna to be shutdown, the Carrier NOC will require the information listed on the sticker to identify the antenna.

## Slide 9: Nardalert S3
Simple to use – Just turn it on and it is ready for use
Pre-configured according to Verizon specifications
Options menus are locked, as there is nothing to adjust
The up and down arrow menu buttons are not functional, except to turn on the display backlight.
Color LCD Display
Protective Silicon Skin
Replaceable Sensor Module
Multi-Color Alarm LED’s
Battery Compartment
On/Off Button
USB Interface For Charging.
Menu Buttons

## Slide 10: Nardalert S3

## Slide 11: Next Steps
  Complete tech training – target for 1Q17
  Narda rep training
    Specific request from New England but we will extend to all areas
  Additional RF meters to field
    As needed based on scale of cell site deployment
  Coordination with industry standards and power companies

## Slide 12: Resources
  VZ Learn
    VZ95377VZ74705
  FCC link needed
    https://www.fcc.gov/general/radio-frequency-safety-0